## Slide 1
Yaju Rajbhandari
EPS team, ORION Space
yazu.raz007@gmail.com
www.orionspace.com.np
Electrical Power Subsystem development
of Nepal-PQ1
November 5, 2018
1st Asian PocketQube Workshop
Singapore

## Slide 2: Outline
  Basic layout to EPS
  Component to build the system
  Test/Working with the components
  PCB Design

## Slide 3: Basic layout
PV CELLS
MPPT Charger/
Charge controller
Battery
Current Sensor
Payload

## Slide 4: Components
PV panel
  5 faces with 8 cells each.
Charging Circuit
  3 SPV 1040 based MPPT
  Battery
  CAS.NP-40

## Slide 5: Spv1040 High efficiency solar battery charger with embedded mppt
Key Features
0.3V to 5.5V operating input voltage
Output voltage regulation, overcurrent and over temperature protection
Up to 95% efficiency

## Slide 6: PV CELLS Currently working with test of charging circuit
Specifications:
Voc=2.2V
Isc=220mA
Vmp=1.92V
Imp=200mA
Pmp=400mW
Efficiency=11.1%
Dimension=60*60*2.5

## Slide 7: PV CELLS
Trisolx Specifications:
Voc=2.62V
Vmp=2.33V
Imp=14.6mA
Pmp=34mW
Efficiency=28%
Dimension=8*26.3*0.16
From TrisolX
Total = 8*14.6 =116.8 mA

## Slide 8: Battery Pack
CAS.NP-40
  Lithium-ion
  3.7V
  1600mAh
  Camera Battery
Battery Protection Circuit
Battery with Protection Circuit
Battery without Protection Circuit

## Slide 9: Development Status of EPS

## Slide 10: Development Boards
STEVAL-ISV006V2
SPV1040 based battery charger with battery charge control circuit.
STEVAL-ISV012V1
SPV1040 based battery charger with L6924D charging circuit, having three charging modes:
  Pre-charge constant current
  Fast-charge constant current
  Constant Voltage

## Slide 11: Battery Charger
Maximum current observed using this board was 75mA using 60*60 solar panel.
Chart: 

## Slide 12: Battery Charger
Chart: 
Chart: Charging Current (mA)

## Slide 13: Battery discharging
Using a resistor of around 7ohm as a load to draw current in the range of 500mA, considering the extreme case.
Chart: Load Voltage (V)
Column1
Chart: Output Current (mA)

## Slide 14
Prototyping
INA219 Prototyping Board
EM v1 Prototyping Board

## Slide 15: Thank You!!!!