## Slide 1: FEC Scheme and Multi-Session support for PocketQubes
Oliver Vassallo
Aaron Abela Dr Ing. Marc A. Azzopardi Prof Ing. Victor Buttigieg Charles Grech
Notes: Good Afternoon, I am Oliver Vassallo and for the next few minutes I shall be presenting the integration of a Forward Error Correction Scheme with Multi-Session Support for PocketQubes

## Slide 2: Introduction
University of Malta M.Sc. Student
Part of the ASTREA Team
Designing the Radio on board the satellite
1 of 17

## Slide 3: Presentation Outline
Introduction
The Project & System Specifications
Comms. Module Operating Modes
Data Link
The Proposed Protocol
Conclusion
2 of 17

## Slide 4: The Project & System Specifications

## Slide 5: The UoMBSat-1 Project - Overview
1p PocketQube Pico-Satellite
Contains an Impedance Probe to characterise the Earth’s Ionosphere
Orbit at around 500km
An 8-minute (max) communication window
Reduce power consumption where possible
3 of 17

## Slide 6: The UoMBSat-1 Project - COMMS System
  Phased Array Ground Station with Digital Combiner
  Forward Error Correction (FEC) Scheme Development
  Radio electronics design
  My contribution:
  The radio electronic design (both hardware and software) and the integration of the FEC scheme
4 of 17

## Slide 7: Top Level DESIGN
5 of 17

## Slide 8: System Requirements
Receiver Sensitivity: -106dBm (25.12fW)
Transmitting Power: 27dBm
Average Orbital Power: 75mW
Bandwidth: 20-25kHz
Frequency: UHF Band (435-438MHz)
6 of 17
Notes: Two most important requirements in a transceiver are the receiver’s sensitivity and the transmitter’s output power. For this project, both were obtained using a link budget and found to be -106dBm and 27dBm respectively. The designed system must be able to achieve these, while consuming around 75mW of average orbital power and fitting on a 42x42mm board. To aid, the processor that shall be used is the Secube, which strikes a balance between the processing power and requiring a small footprint.

## Slide 9: Comms. Module Operating Modes

## Slide 10: Satellite Operating Modes
Total of 5 Modes:
  Mode 0 - Listening Mode
  Mode 1 - Basic Telemetry Mode
  Mode 2 - Detailed Telemetry Mode
  Mode 3 - Logging Mode
  Mode 4 - Critical Maintenance Mode
7 of 17
A high integrity comms. link
Simple & basic comms. link

## Slide 11: Mode 4 – Critical Maintenance Mode
Alter behavior of individual controllers
Send firmware updates
Perform manoeuvres
Get controller feedback
8 of 17

## Slide 12: Mode 4 – Critical Maintenance Mode
Send data with high reliability (such as firmware updates)
Communicate with more than 1 controller (More than 1 session)
By-pass the On-Board Computer
Establish an easier queue system between the ground station and the satellite
Utilize the time window in the most efficient way
8 of 17

## Slide 13: Why do we need an FEC Scheme?
Pros
Reduce re-transmissions
Increase link efficiency
Improve the link reliability
Allow the receiver to operate at a lower SNR
Cons
Increase in processing power, thus power consumption
Encoding & Decoding takes longer
Increase in overhead due to the introduction of redundant bits
9 of 17

## Slide 14: Data Link

## Slide 15: Protocol Comparison
10 of 17
Characteristics | AX.25 | FX.25
Use within the radio community | High | Low
Ability to address more than 1 controller | Not possible without additional layers | Not possible without additional layers
Packet synchronization | Obtained by searching for the flag | Obtained by searching for the correlation tag
Packet compatibility | N/A | Compatible with AX.25 receivers
Packet overhead | Requires bit-stuffing, which reduces the data rate | Requires bit-stuffing and parity bits, reducing data rate
Ability to utilize more than 1 session | Not possible without additional layers | Not possible without additional layers
Encoding/Decoding time | Simple to encode & decode | More complex to encode & decode
Bit Error Rate | Depends on the Eb/No chosen | Adds coding gain due to error correction

## Slide 16: Proposed Protocol – MT.25

## Slide 17: MT.25 – Multiple Frames
Multiple cascaded packets
Each packet starts with a correlation tag, that serves as a packet delimeter.
11 of 17

## Slide 18: MT.25 – Individual Packets
Fixed packet length
Eliminate the need for bit-stuffing to increase user data rate
Same CRC algorithm as used by the AX.25
Low Density Parity Checker (LDPC)
12 of 17

## Slide 19: Proposed Protocol – Header Breakdown
Allows multiple sessions
Reduced header length
13 of 17

## Slide 20: Protocol Comparison
 | AX.25 | FX.25 | MT.25
Payload Length | 251 bytes | 251 bytes | 256 bytes
Overhead Length | 23 bytes | 23 bytes | 12 bytes
Additional Bit-Stuffing bytes – Worst Case | 55 bytes | 55 bytes | -
FEC Block – N = 1057, K = 813 | - | 99 bytes | 80 bytes
Correlation Tag | - | 8 bytes | 8 bytes
Total bytes per packet | 329 bytes | 436 bytes | 356 bytes
14 of 17
User Data | 76% | 58% | 66%

## Slide 21: Protocol Improvement
15 of 17
FEC Code –
N = 1057, K = 813

## Slide 22: FEC vs AX.25
For a given BER of 10-4dB:
  MT.25 & FX.25 have Eb/No of 5dB
  AX.25 has a Eb/No of of 8dB
  Code gain of 3dB
Comparing MT.25 with the AX.25
  3dB coding gain comes at a cost of transmitting at least 8% more bytes
16 of 17

## Slide 23: Conclusion

## Slide 24: Conclusion
Combination of the benefits of 2 protocols – AX.25 & FX.25
Using the link more effectively
Reducing power consumption on the satellite
Improved BER for the same SNR
Provide a new challenging opportunity for the radio community
17 of 17

## Slide 25: Thank you for your Attention!

## Slide 26: Questions?

## Slide 28: Extra Slides

## Slide 29: Modes of Operation – State Machine
Extra Slide