## Slide 1: PocketQube Workshop 2019
Oriol cortés, Aerospace engineering student. Universidad europea de Madrid
oriolcortes1995@Gmail.com

## Slide 2: Project Description

## Slide 3: Project Description
Made by UEM Undergrad Students and AMSAT EA Radio Amateurs

## Slide 4: Project Description
Made by UEM Undergrad Students and AMSAT EA Radio Amateurs
Low Earth Orbit satellite for voice communications
  Intended for FM handheld transceivers

## Slide 5: Project Description
Made by UEM Undergrad Students and AMSAT EA Radio Amateurs
Low Earth Orbit satellite for voice communications
  Intended for FM handheld transceivers
PocketQube 2P 5x5x11.4cm + Base Plate (PocketQube Standard Issue 1)

## Slide 6: Project Description
Made by UEM Undergrad Students and AMSAT EA Radio Amateurs
Low Earth Orbit satellite for voice communications
  Intended for FM handheld transceivers
PocketQube 2P 5x5x11.4cm + Base Plate (PocketQube Standard Issue 1)
Use of COTS components

## Slide 7: Project Description
Made by UEM Undergrad Students and AMSAT EA Radio Amateurs
Low Earth Orbit satellite for voice communications
  Intended for FM handheld transceivers
PocketQube 2P 5x5x11.4cm + Base Plate (PocketQube Standard Issue 1)
Use of COTS components
Use of the difference of Temperatures of the Inside and Outside of the Structure to generate usable Power
  Stirling Engine
  Peltier / Thermoelectric Effect

## Slide 8: Objectives of the Satellite

## Slide 9: Objectives of the Satellite
Learning & Sharing (Open Source)
  Made by Students and Radio Amateurs

## Slide 10: Objectives of the Satellite
Learning & Sharing (Open Source)
  Made by Students and Radio Amateurs
Testing a “new” power source in the new Space industry
  Requires good thermal control

## Slide 11: Objectives of the Satellite
Learning & Sharing (Open Source)
  Made by Students and Radio Amateurs
Testing a “new” power source in the new Space industry
  Requires good thermal control
Provide a Linear Transponder for Radio Amateurs in LEO that anyone can use with a handheld device
  Requires long monopole antennas and high power

## Slide 12: Main Engineering Challenges

## Slide 13: Main Engineering Challenges
Communications
  Unfolding Mechanism for the Antennas
  Non directional antennas + passive attitude control

## Slide 14: Main Engineering Challenges
Communications
  Unfolding Mechanism for the Antennas
  Non directional antennas + passive attitude control
Power Budget
  Low Surface Area
  High power demand of the Linear Transponder

## Slide 15: Main Engineering Challenges
Communications
  Unfolding Mechanism for the Antennas
  Non directional antennas + passive attitude control
Power Budget
  Low Surface Area
  High power demand of the Linear Transponder
ADCS in small satellites

## Slide 16: Main Engineering Challenges
Communications
  Unfolding Mechanism for the Antennas
  Non directional antennas + passive attitude control
Power Budget
  Low Surface Area
  High power demand of the Linear Transponder
ADCS in small satellites
Feasibility of a Stirling Engine as Power source

## Slide 17: Main Engineering Challenges
Communications
  Unfolding Mechanism for the Antennas
  Non directional antennas + passive attitude control
Power Budget
  Low Surface Area
  High power demand of the Linear Transponder
ADCS in small satellites
Feasibility of a Stirling Engine as Power source
Self designed and built Structure and PCBs

## Slide 18: Main Engineering Challenges
Communications
  Unfolding Mechanism for the Antennas
  Non directional antennas + passive attitude control
Power Budget
  Low Surface Area
  High power demand of the Linear Transponder
ADCS in small satellites
Feasibility of a Stirling Engine as Power source
Self designed and built Structure and PCBs
Long Lifespan of the Satellite (~3 years)

## Slide 19: EASAT-2 Solutions

## Slide 20: EASAT-2 Solutions
Nitinol Antennas

## Slide 21: EASAT-2 Solutions
Nitinol Antennas
Inclination of the Magnet of the PMAC to point the antennas parallel to the ground over Europe and similar latitudes

## Slide 22: EASAT-2 Solutions
Nitinol Antennas
Inclination of the Magnet of the PMAC to point the antennas parallel to the ground over Europe and similar latitudes
Spend Resources (€) on buying high performance Solar Panels

## Slide 23: EASAT-2 Solutions
Nitinol Antennas
Inclination of the Magnet of the PMAC to point the antennas parallel to the ground over Europe and similar latitudes
Spend Resources (€) on buying high performance Solar Panels
Focus efforts on precise Thermal design

## Slide 24: EASAT-2 Solutions
Nitinol Antennas
Inclination of the Magnet of the PMAC to point the antennas parallel to the ground over Europe and similar latitudes
Spend Resources (€) on buying high performance Solar Panels
Focus efforts on precise Thermal design
Use of Multi-Layered Insulation + Aluminum Box-like Structure

## Slide 25: EASAT-2 Solutions
Nitinol Antennas
Inclination of the Magnet of the PMAC to point the antennas parallel to the ground over Europe and similar latitudes
Spend Resources (€) on buying high performance Solar Panels
Focus efforts on precise Thermal design
Use of Multi-Layered Insulation + Aluminum Box-like Structure
Fail Safe Electronic Design and avoid Integrated Circuits

## Slide 26: EASAT-2 Solutions
Nitinol Antennas
Inclination of the Magnet of the PMAC to point the antennas parallel to the ground over Europe and similar latitudes
Spend Resources (€) on buying high performance Solar Panels
Focus efforts on precise Thermal design
Use of Multi-Layered Insulation + Aluminum Box-like Structure
Fail Safe Electronic Design and avoid Integrated Circuits
Keep it as simple as possible while accomplishing objectives

## Slide 27: Monopole Antennas
Notes: To be able to use the satellite as a relay of radio amateur frequencies it was decided to use monopole wavelength antennas, which measure 1.03m (half wavelength) and 0.69m, 145.9MHz VHF uplink and 436MHz UHF downlink respectively (approximate measures, might change).
This would allow for radio amateurs to use low gain transmission and reception antennas, which in general, have lower cost, to use EASAT2-UESAT1 as a relay. One of the objectives is that anyone with a Walkie Talkie and a small antenna should be able to use it.

## Slide 28: Unfolding Mechanism of the Antennas
  Shape-Memory Alloys –> Nitinol

## Slide 29: ACS – Passive Magnetic Attitude Stabilization System
Hysteresis rods
Permanent magnet
Non-controlled rotation

## Slide 30: ACS – Passive Magnetic Attitude Control

## Slide 31: ACS – Passive Magnetic Attitude Control

## Slide 32: On-board Processor
8 bit / 4MHz COTS microcontroller (microchip 18F45K22 (same as 50$SAT))

## Slide 33: On-board Processor
8 bit / 4MHz COTS microcontroller (microchip 18F45K22 (same as 50$SAT))
Sends telemetries: temperatures, voltages, internal counters, etc.

## Slide 34: On-board Processor
8 bit / 4MHz COTS microcontroller (microchip 18F45K22 (same as 50$SAT))
Sends telemetries: temperatures, voltages, internal counters, etc.
Receives telecommands: remote switch-off, squelch level,...

## Slide 35: On-board Processor
8 bit / 4MHz COTS microcontroller (microchip 18F45K22 (same as 50$SAT))
Sends telemetries: temperatures, voltages, internal counters, etc.
Receives telecommands: remote switch-off, squelch level,...
Lithium battery monitoring and charging control
  Safe voltage/temperature ranges, charge accounting

## Slide 36: On-board Processor
8 bit / 4MHz COTS microcontroller (microchip 18F45K22 (same as 50$SAT))
Sends telemetries: temperatures, voltages, internal counters, etc.
Receives telecommands: remote switch-off, squelch level,...
Lithium battery monitoring and charging control
  Safe voltage/temperature ranges, charge accounting
Baseband digital signal processing (200samples/s)
  ASK decoder, packet disassembly, CRC, FEC
  ASK encoder
  ALC automatic level control (constant output power)

## Slide 37: On-board Processor
8 bit / 4MHz COTS microcontroller (microchip 18F45K22 (same as 50$SAT))
Sends telemetries: temperatures, voltages, internal counters, etc.
Receives telecommands: remote switch-off, squelch level,...
Lithium battery monitoring and charging control
  Safe voltage/temperature ranges, charge accounting
Baseband digital signal processing (200samples/s)
  ASK decoder, packet disassembly, CRC, FEC
  ASK encoder
  ALC automatic level control (constant output power)
Squelch activation
  (if nobody uses the transponder, we send solar power to bat)

## Slide 38: On-board Processor
EASAT2 analog-digital signal chain

## Slide 39: EPS – Circuit Board

## Slide 40: EPS – Solar Panels
4 x AZUR 3G26.6 ~10k€
Generate ~1W each

## Slide 41: EPS – Testing

## Slide 42: Linear Transponder VHF  UHF Circuit
Notes: The reception and emission subsystem of EASAT2-UESAT1 is based on a linear transponder VHF -> UHF, made out of discrete components (transistors, condensers, etc.) without any integrated board. It is required of the subsystem to be very resistant to failures due to radiation to increase the useful lifespan of the satellite. Its reception band is VHF and transmission band is UHF. It can work with any communication in FM, SSB or any digital modes of low energy. The linear transponder will copy any transmission that is registered above the general noise in a certain dynamic threshold in the VHF band to the UHF band and transmitted back to ground.

## Slide 43: Stirling Engine
Difference in Temperature between the inside and the outside of the MLI to generate power & dissipate heat
Free Piston Stirling Engine
Design currently on hold
Peltier Module could be used instead
Notes: The reception and emission subsystem of EASAT2-UESAT1 is based on a linear transponder VHF -> UHF, made out of discrete components (transistors, condensers, etc.) without any integrated board. It is required of the subsystem to be very resistant to failures due to radiation to increase the useful lifespan of the satellite. Its reception band is VHF and transmission band is UHF. It can work with any communication in FM, SSB or any digital modes of low energy. The linear transponder will copy any transmission that is registered above the general noise in a certain dynamic threshold in the VHF band to the UHF band and transmitted back to ground.

## Slide 44: Thermal Design – Preliminary Simulation

## Slide 45: Thermal Design – Stirling Simulation

## Slide 46: Thermal Design – Electronics Temp.
Chart: 

## Slide 47: Mechanical Design – 1st Iteration

## Slide 48: Mechanical Design – 2nd Iteration

## Slide 49: PocketQube Workshop 2019
THANK YOU FOR YOUR ATTENTION
FEEL FREE TO ASK ANY QUESTIONS
oriolcortes1995@Gmail.com contacto@amsat-ea.org